## Slide 1: NuMicro Timer & WDT & WWDT & RTC & UART
NuMicro@nuvoton.com
Notes: Dear partners, welcome to Nuvoton to attend the NUC100 Workshop.
The objective is to make you understand the architecture, capability of the NUC100, and operation of each peripherals.
1st, we have a 2 days workshop, and 1st day will focus on the marketing, general part of Cortex-M0, and NUC100, then we has a introduction to the H/W board design, and tools, and a tool installation and practice.
For the 2nd day, tomorrow, we will have “document center” and “ISD introduction”, then will start the detailed introduction for the peripherals, and the last section is the porting from Cortex-M3 to Cortext-M0. We also have a “wrap-up” sections to have the summary for these 2 days workshop.
You can raise questions in any time, our designer will be here to give you a comprehensive answer.

## Slide 2: 内容
4组24-bit 定时器带 8-bit 预分频
一个 18-bit 看门狗
一个窗看门狗
带日历的实时时钟
5组完全可编程的 UART.
  2组独立的UART
    支持自动流控功能
    支持 IrDA SIR 功能
    支持 LIN break 功能
  3组Smart-Card 接口支持UART 模式
Notes: My presentation includes 24 bit timer, 19bit watch dog timer, real time clock with calendar function and UART.
I’d like to tell about their feature and structure and then show you some sample codes.

## Slide 3: 定时器特性
4组24-bit 上数定时器
每个定时器有5个时钟源可选和一个预分频
超时周期 = (定时器工作时钟周期) * (8-bit Prescale + 1) * (24-bit TCMP)
支持唤醒 CPU
支持 GPIO 端口状态shadow register
4种计数模式
  单次, 循环, 触发和连续计数模式
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 4: 定时器的时钟源
Notes: Support five kinds of clock source, and the high speed is 22Mhz or the low speed is 32khz. Besides, if selecting clock source is GPIO, the frequent is defined by external input signal. It will count rising edge.

## Slide 5: 定时器方块图 (1/2)
TMRx Clock
& Event Input
Capture Input
Interrupt
Counter Logic
Notes: Main block is 24-bit up counter. The count speed is controlled by clock source and prescale.
If the number of up counter equals TCMPR, timer will generate reset up-counter signal or interrupt to do something. The equation is below.
Besides, up-counter supports read back function.

## Slide 6: 定时器方块图(2/2)
Timer0 Event Input
Inter-Timer Trigger Mode
Timer1
Capture
Notes: Main block is 24-bit up counter. The count speed is controlled by clock source and prescale.
If the number of up counter equals TCMPR, timer will generate reset up-counter signal or interrupt to do something. The equation is below.
Besides, up-counter supports read back function.

## Slide 7: 定时器功能列表
定时器计数模式(1)
事件计数模式(2)
捕获模式:
  Free Counting Mode (3)
  Trigger Counting Mode (4)
计数器复位模式(5)
Inter-Timer Trigger Mode (6)
  计数来自TMR0/TMR2 外部事件引脚的事件
  触发 TMR1/TMR3 锁存计数器的值 TMRx_CAP
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 8: 定时器功能选择: TMRx_CTL Setting
Counter Input TMRx_CTL register |  |  |  |  |  | TMRx clock Input | Event Pin Input *1
INTR_TRG_EN | TCAP_CNT_MOD | TCAP_MODE | TCAP_EN | TMR_EN | MODE_SEL | EVENT_EN = 0 | EVENT_EN = 1
[24] | [20] | [17] | [16] | [0] | [5:4] | [12] | [12]
0 | x | x | 0 | 1 | 0,1,2,3 | Timer Counting Mode | Event Counting Mode
0 | 0 | 0 | 1 | 1 | 0,1,2,3 | Timer Counter Capture Function: “Free Counting Mode” | 
0 | 1 | 0 | 1 | 1 | x | Timer Counter Capture Function: “Trigger Counting Mode” *2 | 
0 | x | 1 | 1 | 1 | 0,1,2,3 | Timer Counter Reset Function | 
1 | x | x | 0 | x | x | x | (TMR0, TMR2)
0 | x | x | 1 | x | x | (TMR1, TMR3) | x
*1 If use “event pin input”, timer cannot set to toggle mode (MODE_SEL=2)
*2 If use “Trigger Counting Mode” or “Inter-Timer Trigger Mode”, the MODE_SEL are don’t care
Inter-Timer Trigger Mode *2

## Slide 9: 定时器计数模式
One shot
0
Ex: TCMPR=100
100
Periodic
0
100
Interrupt
Auto-reload counting
101
224-1
Toggle
0
100
Reset counter
Overflow
0
100
Toggle Output :
TM0→PB8 , TM1→PB9
TM2→PB10 , TM3→PB11
Reset counter
Notes: There are three operation modes, one shot, periodic and toggle mode.
Once TCMPR is set 100, you will find the 24-bit up counter count from 0 to 123 and produce a interrupt. This behavior only executes one time at one shot mode. If change to periodic mode, it will reset counter and repeat counting from 0 to 123 till software stop. If change to toggle mode, it will continuously count to maximum value and overflow to return to 0.

## Slide 10: 捕获模式: Free Counting Mode
1. Any rising/falling edge event always latch the TMRx counter value to TMRx_TCAP register and set TCAP_IS status
2. High level time, TH = (10 – 6) / TMRx_CLK
3. When edge event occur in TCAP_IS period, the timer will drop the new capture value and set NCAP_DET_IS flag
1
1
3
TH
2
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 11: 捕获模式: Trigger Counting Mode
1. An rising edge event, reset the TMRx counter value to zero and trigger counter counting
2. An falling edge event, latch the TMRx counter value to TMRx_TCAP register and set TCAP_IS status
3. High level time, TH = 2 / TMRx_CLK
TH
1
2
3
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 12: 计数器复位功能
1. Any rising/falling edge event always reset the TMRx counter value to zero and set TCAP_IS status
1
1
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 13: Inter-Timer Trigger Mode (1/2)
1. Enable TMR0_CTL.INTR_TRG_EN will start TM0 pin event counting and generate a “INTR_TMR_TRG” signal to trigger TMR1
2. When TMR0 counter equal to TMR0_CMPR, the “INTR_TMR_TRG” signal will stop and latch TMR1 counter value to TMR1_TCAP register and set TMR1_ISR.TCAP_IS status
1
2
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 14: Inter-Timer Trigger Mode (2/2)
3. At the same time TMR0 INTR_TRG_EN bit will set to 0, TMR0 and TMR1 stop counting
4. TTM0 = TMR1_TCAP / TMR1_CLK / TMR0_CMPR = 999 / 100kHz / 100 = 100 us
FTM0 = TMR1_CLK / TMR1_TCAP × TMR0_CMPR = 100kHz / 999 × 100 = 10 kHz
3
TTM0
4
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 15: 内部触发事件(1/3)
描述
  当定时器超时或者捕获中断事件发生时，可以产生内部事件启动外设
  支持启动ADC, DAC, PDMA 和Touch-key
中断事件
  定时器超时, TMR_IS
  定时器捕获, TCAP_IS
Power-down 模式下唤醒触摸键
  不唤醒CPU
  这个模式支持来自定时器TMR0的TMR_IS 事件
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 16: 内部触发事件 (2/3)
1. 当定时器超时或者捕获中断发生时，产生一个内部触发事件，触发外设开始工作
2. 当CPU 在掉电模式时, TMR0 支持产生超时唤醒事件触发Touch-key 控制器 (TMR0 时钟源可以选择32kHz or 10kHz)
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 17: 内部触发事件(3/3)
Internal Trigger Event (Target Peripherals) Trigger State | PDMA_TEEN = 1 (PDMA) | DAC_TEEN = 1 (DAC) | ADC_TEEN = 1 (ADC) | TK_TEEN = 1 (Touch Key)
CAP_TRG_EN = 0 | Trigger with TMR_IS |  |  | Trigger with TMR_IS or TCAP_IS *1
CAP_TRG_EN = 1 | Trigger with TCAP_IS |  |  | 
*1 TCAP_IS 事件不支持从掉电模式唤醒Touch-key, 只有 TMR_IS 事件才可以.
Notes: Let me begin explaining timer feature.
NUC100 supports four sets of 24 bit up counting timer
And every timer has five selection of clock source and a prescale.
Once the clock source and prescale are defined, you can use this equation to calculate the time out period.
Besides, timer support three modes and explain it later.

## Slide 18: 定时器范例
定时器代码
  使能TM0 功能引脚
  使能 Timer0 反转模式
  设定超时周期为 1 second
  Timer0 中断处理函数
Notes: At this presentation, we support two RTC examples. The first example, we use library to open RTC and install a alarm callback function. Second, we directly control RTC special register to do the same flow.

## Slide 19: 定时器代码(1/2)
//----------------------------------------------------------------------------
// MAIN function
//----------------------------------------------------------------------------
volatile uint32_t TMR0_Counter = 0;
int32_t main (void)
{
UNLOCKREG();
CLK->PWRCTL |= CLK_PWRCTL_HXT_EN;
while(!(CLK->CLKSTATUS & CLK_CLKSTATUS_HXT_STB));
LOCKREG();
//Setting TMR0 Clock Source and Enable TMR0 Clock
CLK->CLKSEL1 = (CLK->CLKSEL1 & ~CLK_CLKSEL1_TMR0_MASK) | CLK_CLKSEL1_TMR0_HXT;
CLK->APBCLK |= CLK_APBCLK_TMR0_EN;
//Enable TM0 pin (@PB.8)
GCR->PB_H_MFP = (GCR->PB_H_MFP & ~ PB8_MFP_MASK) | PB8_MFP_TMR0_EXT;
//Setting TMR0 to Toggle Mode
TIMER_Init(TIMER0, 11, 1000000, TIMER_CTL_MODESEL_TOGGLE);
TIMER_EnableInt(TIMER0, TIMER_IER_TMRIE);
TIMER_Start(TIMER0);
while(1);
}
Setting TMR0 clock source
Enable TM0 pin
设定TMR0 为反转模式, 使能中断并启动TMR0
超时周期= 12 MHz * (11 + 1) * 1000000 = 1.0 second
Notes: First, open timer. Its parameter is timer0 and periodic mode and its time interval is 2 tick per second.
Second, install callback function and execute it every 2 ticks.
Program will execute timer delay until this parameter equals 10.
The delay time is 4 ticks (2 second).

## Slide 20: 定时器代码(2/2)
//----------------------------------------------------------------------------
// TMR0 IRQ handler
//----------------------------------------------------------------------------
void TMR0_IRQHandler(void)
{
//TMR0 Timeout Interrupt Status is Set
if(TIMER0->ISR&TIMER_ISR_TMRIS)
{
TIMER0->ISR |= TIMER_ISR_TMRIS; //Clear TMR0 Timeout Interrupt Status
TMR0_Counter++;
printf("TMR0 Timeout: %d\n", TMR0_Counter);
}
//TMR0 Capture Interrupt Status is Set
if(TIMER0->ISR&TIMER_ISR_TCAPIS)
{
printf("TMR0 Capture: %d\n", TIMER0->TCAP); //Clear TMR0 Capture Interrupt Status
TIMER0->ISR |= TIMER_ISR_TCAPIS;
}
}
When TMR0 timeout interrupt
When TMR0 capture interrupt
Notes: First, open timer. Its parameter is timer0 and periodic mode and its time interval is 2 tick per second.
Second, install callback function and execute it every 2 ticks.
Program will execute timer delay until this parameter equals 10.
The delay time is 4 ticks (2 second).

## Slide 21: 看门狗特性
18-bit 上数计数器
8 个超时间隔可选
4 个WDT 复位延迟时间可选
功能:
  WDT 中断
  WDT 复位
  WDT 唤醒
Notes: WDT includes 18 bit up counter and eight time out selections, and also support interrupt, reset and wakeup function.

## Slide 22: WDT 时钟源

## Slide 23: WDT 方块图
WDT 可以导致WDT 中断或者 在一个固定的延迟周期之后复位.
WDT 也可以将CPU从掉电模式唤醒
Notes: You’ll see that the main block is 18-bit WDT counter. Once the WTE is set, 18bit WDT counter will start to count and then produce a time out signal if the counter over time out period. This signal will generate interrupt if you enable interrupt function and also can wake up CPU at power down mode. It also can reset system like POR reset after 1024 WDT clocks. Besides, you don’t want to see any time out signal. You can set WTR to reset WDT counter.

## Slide 24: WDT 超时间隔选择
WTIS *1 | WDT Timeout Interval | WDT Reset Interval *2 | WDT Timeout Interval (WDT_CLK = 10kHz) | WDT Reset Interval (WDT_CLK = 10kHz)
0 | 24 × TWDT_CLK | (24 + Delay Clock) × TWDT_CLK | 1.6 ms | 1.9 ms ~ 104.2 ms
1 | 26 × TWDT_CLK | (26 + Delay Clock) × TWDT_CLK | 6.4 ms | 6.7 ms ~ 109.0 ms
2 | 28 × TWDT_CLK | (28 + Delay Clock) × TWDT_CLK | 25.6 ms | 25.9 ms ~ 128.2 ms
3 | 210 × TWDT_CLK | (210 + Delay Clock) × TWDT_CLK | 102.4 ms | 102.7 ms ~ 205.0 ms
4 | 212 × TWDT_CLK | (212 + Delay Clock) × TWDT_CLK | 409.6 ms | 409.9 ms ~ 512.2 ms
5 | 214 × TWDT_CLK | (214 + Delay Clock) × TWDT_CLK | 1.6384 s | 1.6387 s ~ 1.7410 s
6 | 216 × TWDT_CLK | (216 + Delay Clock) × TWDT_CLK | 6.5536 s | 6.5539 s ~ 6.6562 s
7 | 218 × TWDT_CLK | (218 + Delay Clock) × TWDT_CLK | 26.2144 s | 26.2147 s ~ 26.3170 s
*1 WTIS(WDT_CTL[6:4]) 选择看门狗超时间隔.
*2 “Delay Clock” 可以选择3, 18, 130 and 1026, select by WTRDSEL(WDT_CTL[9:8])
Notes: This table list all time out selections. If we select the level 0, system will produce a interrupt after sixteen WDT clock. And produce a reset signal after 1040 WDT clock. If the clock source is 12Mhz, the WDT time out interval for reset is 86.67us. And clock source is 32khz, the timeout interval is 32.5ms. Based on different application, you set WTIS to select the time out period you want.

## Slide 25: WDT 范例
WDT 代码
  设定WDT 超时间隔“216 × TWDT_CLK”
  设定WDT 复位延迟“1026 WDT_CLK 时钟周期”
  WDT 中断处理函数
  检查WDT 唤醒事件
  检查WDT 复位事件
Notes: At this presentation, we support two RTC examples. The first example, we use library to open RTC and install a alarm callback function. Second, we directly control RTC special register to do the same flow.

## Slide 26: WDT 代码(1/2)
//----------------------------------------------------------------------------
// MAIN function
//----------------------------------------------------------------------------
int main (void)
{
UNLOCKREG();
CLK->PWRCTL |= CLK_PWRCTL_HXT_EN | CLK_PWRCTL_LIRC_EN;
while(!(CLK->CLKSTATUS & (CLK_CLKSTATUS_HXT_STB | CLK_CLKSTATUS_LIRC_STB )));
LOCKREG();
//Checking WDT Reset Flag of System Reset Source Register
if(GCR->RST_SRC & GCR_RSTSRC_WDT)
{
GCR->RST_SRC |= GCR_RSTSRC_WDT; //Clear WDT Reset Status
printf(“System Reset from WDT Timeout !\n”);
}
//Enable Watchdog Timer
WDT_Init(WDT_CTL_WTIS_2POW14, WDT_CTL_WTRDSEL_1026CLK);
WDT_EnableInterrupt();
WDT_START;
while(1);
}
Enable internal 10kHz RC
Enable WDT interrupt and start WDT
WDT Timeout Interval = 214 WDT clocks
WDT reset delay: 1026 WDT clocks
Check WDT reset status on system power-on

## Slide 27: WDT 代码(2/2)
//----------------------------------------------------------------------------
// WDT IRQ handler
//----------------------------------------------------------------------------
void WDT_IRQHandler(void)
{
//WDT Interrupt Status is Set
if(WDT->ISR & WDT_ISR_WDTIS)
{
WDT->ISR |= WDT_ISR_WDTIS; //Clear WDT Interrupt Status
WDT_RESET_TIMER; //Reset WDT Timer Counter
printf("WDT interrupt !!!\n”);
}
//WDT Wake-up Status is Set
if(WDT->ISR & WDT_ISR_WDTWAKEIS)
{
WDT->ISR |= WDT_ISR_WDTWAKEIS; //Clear WDT Wake-up Status
printf("WDT Wake-up!\n”);
}
}
When WDT interrupt
When WDT after Wake-up

## Slide 28: 窗看门狗特性
6-bit 下数计数器和比较器
  使WWDT 窗周期更有弹性
16 个WWDT预分频计数器可选
  WWDT 超时间隔可选
芯片复位之后只可以写一次 WWDT 控制寄存器，否则系统将复位
  软件无法关闭WWDT, 或者改变任何设定
WWDT 和WDT 共享一个 IRQ 中断号
支持的功能:
  WWDT 中断
  WWDT 复位
Notes: WDT includes 18 bit up counter and eight time out selections, and also support interrupt, reset and wakeup function.

## Slide 29: 窗看门狗时钟源
Notes: WDT includes 18 bit up counter and eight time out selections, and also support interrupt, reset and wakeup function.

## Slide 30: 窗看门狗方块图
WWDT 可以导致WWDT 中断或者 WWDT 复位CPU
16 selections WWDT pre-scale
Reload window setting
Reload WWDT counter
Notes: WDT includes 18 bit up counter and eight time out selections, and also support interrupt, reset and wakeup function.

## Slide 31: WWDT 计数器重载波形
1. 启动WWDTCNT 计数器
2. 当WWDTCNT = WINCMP, WWDTTIF 标志被设为”1”
3. 当在窗口内重载WWDTCNT 时, WWDT 将重新开始计数; ( 0 < WWDTCNT <= WINCMP )
4. 当在窗口外重载WWDTCNT 时, 芯片将被复位，标志WWDTRF 将被设; ( WWDTCNT > WINCMP )
1
2
3
4
Reload
Window
4
Notes: WDT includes 18 bit up counter and eight time out selections, and also support interrupt, reset and wakeup function.

## Slide 32: WWDT计数器重载波形
1. 如果WWDTCNT 计数器下数到0, 芯片将复位，标志 WWDTRF 将被设; ( WWDTCNT == 0 )
1
Reload
Window
Notes: WDT includes 18 bit up counter and eight time out selections, and also support interrupt, reset and wakeup function.

## Slide 33: WWDT 重载窗口计算
*1 PERIODSEL(WWDTCR[11:8]) is pre-scale period select for the WWDT
*2 Start time of WWDT reload window, WINCMP(WWDTCR[11:8) is WWDT compare value
*3 End time of WWDT reload window
PERIODSEL *1 | Prescaler Value | WWDT Reload Window |  | WWDT Reload Window (WINCMP = 32, WWDT_CLK = 12MHz/2048)
 |  | WWDT Compare Period *2 | WWDT Timeout Period *3 | 
0 | 1 | 1 × WINCMP × TWWDT | 1 × 64 × TWWDT | 5.5 ms ~ 10.9 ms
1 | 2 | 2 × WINCMP × TWWDT | 2 × 64 × TWWDT | 10.9 ms ~ 21.8 ms
2 | 4 | 4 × WINCMP × TWWDT | 4 × 64 × TWWDT | 21.8 ms ~ 43.7 ms
3 | 8 | 8 × WINCMP × TWWDT | 8 × 64 × TWWDT | 43.7 ms ~ 87.4 ms
4 | 16 | 16 × WINCMP × TWWDT | 16 × 64 × TWWDT | 87.4 ms ~ 174.8 ms
5 | 32 | 32 × WINCMP × TWWDT | 32 × 64 × TWWDT | 174.8 ms ~ 349.5 ms
6 | 64 | 64 × WINCMP × TWWDT | 64 × 64 × TWWDT | 349.5 ms ~ 699.1 ms
7 | 128 | 128 × WINCMP × TWWDT | 128 × 64 × TWWDT | 699.1 ms ~ 1.3981 s
8 | 192 | 192 × WINCMP × TWWDT | 192 × 64 × TWWDT | 1.0486 s ~ 2.0972 s
9 | 256 | 256 × WINCMP × TWWDT | 256 × 64 × TWWDT | 1.3981 s ~ 2.7962 s
10 | 384 | 384 × WINCMP × TWWDT | 384 × 64 × TWWDT | 2.0972 s ~ 4.1943 s
11 | 512 | 512 × WINCMP × TWWDT | 512 × 64 × TWWDT | 2.7962 s ~ 5.5924 s
12 | 768 | 768 × WINCMP × TWWDT | 768 × 64 × TWWDT | 4.1943 s ~ 8.3886 s
13 | 1024 | 1024 × WINCMP × TWWDT | 1024 × 64 × TWWDT | 5.5924 s ~ 11.1848 s
14 | 1536 | 1536 × WINCMP × TWWDT | 1536 × 64 × TWWDT | 8.3886 s ~ 16.7772 s
15 | 2048 | 2048 × WINCMP × TWWDT | 2048 × 64 × TWWDT | 11.1848 s ~ 22.3696 s
Notes: This table list all time out selections. If we select the level 0, system will produce a interrupt after sixteen WDT clock. And produce a reset signal after 1040 WDT clock. If the clock source is 12Mhz, the WDT time out interval for reset is 86.67us. And clock source is 32khz, the timeout interval is 32.5ms. Based on different application, you set WTIS to select the time out period you want.

## Slide 34: WWDT 范例
WWDT 代码
  设定WWDT 预分频为 512 ，控制 WWDT 下数的速度
  设定WWDT 比较寄存器的值 0x20
  WDT IRQ 中断处理函数中检查WWDT 中断标志
  WWDT 复位示例
Notes: At this presentation, we support two RTC examples. The first example, we use library to open RTC and install a alarm callback function. Second, we directly control RTC special register to do the same flow.

## Slide 35: WWDT 代码(1/2)
uint32_t volatile wwdt_cnt = 0;
//----------------------------------------------------------------------------
// MAIN function
//----------------------------------------------------------------------------
int main (void)
{
UNLOCKREG();
CLK->PWRCTL |= CLK_PWRCTL_HXT_EN;
while(!(CLK->CLKSTATUS & CLK_CLKSTATUS_HXT_STB));
LOCKREG();
//Enable Window Watchdog Timer
WWDT_Init(WWDT_CR_PERIODSEL_512, 0x20);
WWDT_EnableInterrupt();
while(1)
{
//After WWDT interrupt 4 times to setup reload WWDT counter chip will reset
if(wwdt_cnt >= 4)
WWDT->RLD = WWDT_RELOAD_KEY;
}
}
Enable WWDT and interrupt

## Slide 36: WWDT 代码(2/2)
//----------------------------------------------------------------------------
// WDT and WWDT share a single IRQ handler
//----------------------------------------------------------------------------
void WDT_IRQHandler(void)
{
//WWDT Interrupt Status Flag is Set
if((WWDT->STS&WWDT_STS_IF))
{
WWDT_RELOAD; //Reload WWDT Prescaler & Counter Value
WWDT->STS = WWDT_STS_IF; //Clear WWDT Interrupt Status
wwdt_cnt++;
printf("INT: %d\n", wwdt_cnt); //Print WWDT Interrupt Times
printf("WWDTVAL: %d\n", WWDT->VAL); //Print WWDT Counter Value
}
}
Chack the WWDT interrupt
Reload WWDT counter

## Slide 37: RTC 特性
只有一组 RTC 计数器和alarm 寄存器
支持 alarm 和time tick 中断
支持唤醒功能
32 kHz 频率补偿
80 bytes RTC spare register 可以用来暂存信息
  支持snoop 引脚清除RTC spare register功能
Register | BCD Value (24-hour) | Written | Description
RTC_TLR | 0x00093043 | AM 09:30:43 | Time Counter
RTC_CLR | 0x00120229 | 2012/02/29 | Calendar Counter
RTC_DWR | 0x00000003 | Wednesday | Day of the Week Counter
RTC_LIR | 0x00000001 | Leap year | Leap Year Indication
RTC_TAR | 0x00100000 | AM 10:00:00 | Time Alarm Value
RTC_CAR | 0x00120301 | 2012/03/01 | Calendar Alarm Value
Notes: WDT includes 18 bit up counter and eight time out selections, and also support interrupt, reset and wakeup function.

## Slide 38: RTC 方块图
INIR
(0xA5EB1357)
AER
(0xA965)
512 RTC clock
≒15msec
Notes: The main block is RTC time counter control unit. And then related registers are Time Load Register, Calendar Load Register, day of week, leap year and hour mode. Another block is alarm function. Once alarm register is equal to Load register, it will produce alarm interrupt if you enable. Third block is time tick function. Based on your selection, it will generate a periodic interrupt.
Besides, you must take care two registers before setup all parameter. The first register is initiation register. We must store A5EB1357 into this register to initial RTC block. The second register is access register. And must be stored A965 to enable access limit. It will auto-disable after 128 RTC clock.
32.768KHZ的晶振产生时序电路基准信号。32.768kHz是RTC（实时时钟）晶振，用32.768是因为32768是2的15次幂，可以很方便的分频，很精确的得到一秒的计时。所有的RTC晶振一般都是32.768或是其倍频。

## Slide 39: RTC 寄存器访问使能
写AER[15:0]=0xA965 可以访问RTC 寄存器
Register | Description | AER[16] = 1 (Access Enabled) | AER[16] = 0 (Access Disabled)
RTC_INIR | RTC Initiation Register (0xA5EB1357) | R/W | R/W
RTC_AER | RTC Access Enable Register (0xA965) | R/W | R/W
RTC_FCR | RTC Frequency Compensation Register | R/W | -
RTC_TLR | Time Loading Register | R/W | R
RTC_CLR | Calendar Loading Register | R/W | R
RTC_TSSR | Time Scale Selection Register | R/W | R/W
RTC_DWR | Day of the Week Register | R/W | R
RTC_TAR | Time Alarm Register | R/W | -
RTC_CAR | Calendar Alarm Register | R/W | -
RTC_LIR | Leap Year Indicator Register | R | R
RTC_RIER | RTC Interrupt Enable Register | R/W | R/W
RTC_RIIR | RTC Interrupt Indication Register | R/W | R/W
RTC_TTR | RTC Time Tick Register | R/W | -
RTC_SPRCTL | RTC Spare Functional Control Register | R/W | -
RTC_SPR0 ~ RTC_SPR19 | RTC Spare Register 0 ~ 19 | R/W | -
Notes: This table list all of RTC register and access limit. Once the AER register is set to A965, the access limit is list here. And after 128 RTC clock, it will be change to this.

## Slide 40: RTC 频率补偿寄存器
对输入的 32kHz crystal 做数字补偿
  输入晶振频率范围: 32776 Hz to 32761 Hz
  频率补偿精度: ±0.4768 ppm
RTC_FCR 寄存器, 设定Input_Clock 值
  RTC_FCR.INTEGER = [Input_Clock(integer part) – 32768] +7
  RTC_RCR.FRACTION = Input_Clock(fraction part) × 64
范例
  外部晶振经测量: 32773.66 Hz
  RTC_FCR.INTEGER = (32773 – 32768) + 7 = 12 => 0x0C
  RTC_RCR.FRACTION = 0.66 × 64 = 39.6 => 0x27
Notes: At this presentation, we support two RTC examples. The first example, we use library to open RTC and install a alarm callback function. Second, we directly control RTC special register to do the same flow.

## Slide 41: RTC 范例
RTC 代码
  使能RTC 并设定时间和日期
    Date: 2012 / 7 / 1
    Time: 13:20:00
  使能alarm 中断并设定alarm date and time
    Alarm date: 2012 / 7 / 1
    Alarm time: 13:20:10
  使能time tick 中断
  在Tick 中断中显示RTC 当前时间
Notes: At this presentation, we support two RTC examples. The first example, we use library to open RTC and install a alarm callback function. Second, we directly control RTC special register to do the same flow.

## Slide 42: RTC 代码(1/2)
//----------------------------------------------------------------------------
// MAIN function
//----------------------------------------------------------------------------
int32_t main (void)
{
S_DRVRTC_TIME_DATA_T sInitTime, sCurTime;
RTC_Init(); // RTC Initialize
// Time Setting
sInitTime.u32Year = 2012;
sInitTime.u32cMonth = 7;
sInitTime.u32cDay = 1;
sInitTime.u32cHour = 13;
sInitTime.u32cMinute = 20;
sInitTime.u32cSecond = 0;
sInitTime.u32cDayOfWeek = DRVRTC_TUESDAY;
sInitTime.u8cClockDisplay = DRVRTC_CLOCK_24;
while(RTC_Open(&sInitTime) != E_SUCCESS); // Initial RTC current time
// The alarm time setting
sCurTime.u32cSecond = sCurTime.u32cSecond + 10;
RTC_WriteAlarm(&sCurTime); // Set the alarm time
RTC_EnableInt(RTC_RIER_AIER); // Enable RTC Alarm Interrupt
RTC_EnableInt(RTC_RIER_TIER); // Enable RTC Tick Interrupt
while(1);
}
Initial RTC
Enable RTC alarm and time tick interrupt

## Slide 43: RTC 代码(2/2)
//----------------------------------------------------------------------------
// RTC IRQ handler
//----------------------------------------------------------------------------
void RTC_IRQHandler(void)
{
S_DRVRTC_TIME_DATA_T sInitTime, sCurTime;
if (RTC->RIIR & RTC_RIIR_AIS) // Alarm interrupt
{
RTC->RIIR |= RTC_RIIR_AIS;
printf("Alarm!!\n");
}
if (RTC->RIIR & RTC_RIIR_TIS) // Tick interrupt
{
RTC->RIIR |= RTC_RIIR_TIS;
RTC_Read(&sCurTime); // Read current time
// Display current time
printf("Current Time: %d/%02d/%02d %02d:%02d:%02d\n",
sCurTime.u32Year, sCurTime.u32cMonth, sCurTime.u32cDay,
sCurTime.u32cHour, sCurTime.u32cMinute, sCurTime.u32cSecond);
}
}
When RTC alarm interrupt
When RTC time tick interrupt, print RTC current time

## Slide 44: UART 特性
2组完全可编程 UART 通道
支持波特率发生器和自动波特率检测
支持自动流控 (/CTS, /RTS)
16-bytes FIFO 用于TX/RX 数据缓存
收到数据或者/CTS 引脚电平变化可以唤醒CPU
支持PDMA收/发UART数据
UART 功能选择
  支持UART, IrDA, LIN 和RS-485 功能
Notes: Let me begin explaining UART features. NUC100 includes up to three fully programmable UART channels. Every channel has independent baud-rate generator, serial interface characteristic setting and entry FIFO for Rx and Tx data payload. UART also support auto flow control, IrDA and LIN break function.

## Slide 45: UART 时钟源
HIRC support hardware auto trim function (need 32 kHz external crystal)
and three target frequency (11.0592 MHz / 12 MHz / 12.288 MHz)
Notes: UART supports 4 clock sources. The maximum is 22Mhz and the minimum is 12Mhz.And then all UART use one 4-bit prescale to divide UART clock source. Besides, we suggest using 22Mhz.

## Slide 46: UART 方块图
Note: 16-bytes TX_FIFO and 16-bytes RX_FIFO
Notes: Once select UART clock source, the baud rate generator will output baud rate signal that you set. And then We also can set data length, parity and stop bit via control and status register. Final, UART can transfer and receiver data via FIFO.

## Slide 47: UART 波特率设定(1/2)
Fully programmable serial interface
Baud rate generator (UARTx_BAUD register)
5 ~ 8bits
Even, odd or no-parity
1 ~ 2bits
Mode | DIV_16_EN *1 | Baud rate equation
Mode 0 | 0 (Disable) | UART_CLK / (BRD + 1), BRD must > 8 *2
Mode 1 | 1 (Enable) | UART_CLK / [(BRD + 1) × 16]
*1 DIV_16_EN is baud rate divider base number at register UARTx_BAUD[31] bit
*2 BRD is baud rate divider number at register UARTx_BAUD[15:0] bits

## Slide 48: UART波特率设定(2/2)
UART clock source = 12 MHz |  | 
Baud rate | Mode 0 (DIV_16_EN=0) *1 | Mode 1 (DIV_16_EN=1)
921600 | BRD=12 *2 | Not Supported
460800 | BRD=25 | Not Supported
230400 | BRD=51 | BRD=2
115200 | BRD=103 | BRD=6
57600 | BRD=207 | BRD=12
38400 | BRD=311 | BRD=19
19200 | BRD=624 | BRD=38
9600 | BRD=1249 | BRD=77
4800 | BRD=2499 | BRD=155
*1 DIV_16_EN is baud rate divider base number at register UARTx_BAUD[31] bit
*2 BRD is baud rate divider number at register UARTx_BAUD[15:0] bits
Notes: Based on 22.1184Mhz, this table lists some standard baud rate.
We suggest the main clock source is 22Mhz and list its related setting. It can easy support standard baud rate.

## Slide 49: UART 自动波特率检查
如果使能自动波特率检测
  UART控制器将测量收到的字节的START比特的时间 (LSB 必须=“1”)
  硬件将自动设定波特率寄存器UARTx_BARD
LSB must be “1”
Notes: This picture is copied from window hyper terminal and show all of UART setting.
First, we must set data length, parity and stop bit. The range of data length is from 5 bits to 8bits. The parity can by set even, odd or no-parity. The range of stop bit is 1bit to 2bits.
Second, baud-rate generator support three equations to generate baud rate you want.

## Slide 50: UART 自动流控功能
支持自动流控功能 (/CTS, /RTS)
/CTS pin可以唤醒CPU
/RTS can trigger /CTS to control when can transfer data.

## Slide 51: UART 唤醒功能 (1/2)
UART CTS pin wake-up, case 1
UART CTS pin wake-up, case 2
1. UART CTS pin can wake-up system, when the rising or falling edge event
2. After wake-up signal, the UART clock will start and set interrupt flag
1
2
1
2
Notes: This picture is copied from window hyper terminal and show all of UART setting.
First, we must set data length, parity and stop bit. The range of data length is from 5 bits to 8bits. The parity can by set even, odd or no-parity. The range of stop bit is 1bit to 2bits.
Second, baud-rate generator support three equations to generate baud rate you want.

## Slide 52: UART唤醒功能 (2/2)
UART 接收数据唤醒
1. UART incoming data can wake-up system, when the “Start Bit” enter
2. After wake-up signal, the UART clock will start and set interrupt flag
1
2
Notes: This picture is copied from window hyper terminal and show all of UART setting.
First, we must set data length, parity and stop bit. The range of data length is from 5 bits to 8bits. The parity can by set even, odd or no-parity. The range of stop bit is 1bit to 2bits.
Second, baud-rate generator support three equations to generate baud rate you want.

## Slide 53: IrDA 功能(1/2)
支持 IrDA 发送或者接收
支持反转功能：IR_SOUT and IR_SIN
Notes: We add IrDA signal generator at UART module. It will transfer UART signal to IrDA signal and IrDA signal to UART signal. And it also support inverse function to inverse IR_SOUT and IR_SIN signal.

## Slide 54: IrDA功能(2/2)
Notes: This timing will be showed how to transfer UART and IrDA signal. At Tx timing, signal will be changed from UART signal to IrDA signal. It will generate pulse at every UART low signal and the pulse width is Three- sixteenth (3/16) bit width. For Rx timing, signal will be changed from IrDA signal to UART signal. It will generate low signal every rising edge of UART signal.

## Slide 55: RS-485 功能
支持硬件或者软件控制 RTSn ，或者软件控制GPIO 来控制传输方向
支持RS-485 硬件地址检测
  Normal Multi-Drop Operation Mode (NMM)
  Auto Address Detection Operation Mode (AAD)
  Auto Direction Mode (AUD)
Notes: This is a LIN frame and includes a break field and four to eleven byte fields. Each byte field is transmitted as a serial byte that use UART format. The break symbol is used to signal the beginning of a new frame and is always generated from master. NUC100 support generate LIN break for Tx and produce a interrupt when Rx receive a break signal.

## Slide 56: LIN 功能
支持 LIN 主/从节点模式
LIN header 选择
  Break field + Sync field + Identifier field
LIN break 域计数设定(master only)
  8-bits ~ 15-bits
Support LIN header and bit error detect interrupt

## Slide 57: UART 范例
UART0 代码
  波特率:115200
  数据长度: 8 bits
  校验 : Disable
  停止位: 1 bit

## Slide 58: UART 代码 (1/2)
//----------------------------------------------------------------------------
// MAIN function
//----------------------------------------------------------------------------
int32_t main (void)
{
STR_UART_T sParam;
uint8_t u8data;
UNLOCKREG();
CLK->PWRCTL |= CLK_PWRCTL_HXT_EN;
while(!(CLK->CLKSTATUS & CLK_CLKSTATUS_HXT_STB));
LOCKREG();
// Select UART clock source and Enable UART0 clock
CLK->CLKSEL1 = (CLK->CLKSEL1 & ~CLK_CLKSEL1_UART_MASK) | CLK_CLKSEL1_UART_HXT;
CLK->CLKDIV0 &= ~CLK_CLKDIV0_UART_MASK;
// Enable UART0 clock
CLK->APBCLK |= CLK_APBCLK_UART0_EN;
// Enable UART0 function pin
MFP_FULL_UART0_TO_PORTA();
Setting UART clock source and divider
Enable UART0 clock
Enable UART0 function pin

## Slide 59: UART代码(2/2)
// Setting and Initial UART0
sParam.u32BaudRate = 115200;
sparam.u32cDataBits = DRVUART_DATABITS_8;
sparam.u32cStopBits = DRVUART_STOPBITS_1;
sparam.u32cParity = DRVUART_PARITY_NONE;
sparam.u32cRxTriggerLevel = DRVUART_FIFO_1BYTES;
sParam.u8EnableDiv16 = DISABLE;
//UART0 Initialize
UART_Init(UART0, &sParam);
//UART transmit and receive test
printf(“Please press any key...\n”);
scanf("%c", &u8data);
printf(“Enter key is: %c\n”, u8data);
while(1);
}
Setting UART baud rate and serial format
Transmit and receive test

## Slide 60: Timer_WDT_RTC示例代码
Nano100BSeriesBSP_CMSIS
NuMicro NANO100B
Driver Reference Guide
Sample
Document
Nu_LB
Timer_WDT_RTC
KEIL
Timer_WDT_RTC. uvproj

## Slide 61: Timer_WDT_RTC 代码说明
TIMER 设定
  时钟源: 12MHz
  Operation mode: Periodic mode
  Time out period = (1/12000000)*(255+1)*(46875) = 1 second
WDT 设定
  时钟源: 10KHz
  WTIS: 0x06
  WDT timeout interval for interrupt = 6.55 s
RTC 设定
  时钟源: 32KHz
  Current time setting: Date09/1/19, time13:20:00
  Alarm time setting: Date09/1/19, time13:20:20

## Slide 62: Timer_WDT_RTC 运行结果
On-board Nu-Link-Me connect to KEIL-IDE debug or programming
UART port: transmit Timer, WDT and RTC information
Reset key, press to reboot Nano100 chip

## Slide 63: Q&A
Thank You
Notes: Thanks for your attention,