## Slide 1: NuMicro Nano SPI
NuMicro@nuvoton.com

## Slide 2: 内容
特性
方块图
功能描述
代码

## Slide 3: 特性 (I)
总共3组SPI 控制器
支持主(最大 32 MHz) 和从 (最大 16 MHz) 模式
每个SPI 控制器能够驱动2个从设备
支持 1-bit (channel) or 2-bit (channel) 串行数据IN/OUT
支持 双重IO 传输模式
每笔传输的bit长度可以配置 (8 to 32 bits)
MSB or LSB first

## Slide 4: 特性(II)
支持 Word- and Byte-暂停功能
主模式下支持可变时钟功能
提供独立的 8-level depth Tx/Rx FIFO
支持唤醒功能
支持PDMA 传输
支持3-wire, 没有从机片选, 双向接口
支持常用的 SPI 时序Mode 0 ~ Mode 3

## Slide 5: 方块图
1-channel I/O
2-channel I/O
x : indicates the number of SPI controller

## Slide 6: SPI 基本功能设定 (I)
Function | Master/Slave SLAVE (SPI_CTL[18]) | LSB First LSB (SPI_CTL[10]) | Bit Length TX_BIT_LEN (SPI_CTL[7:3])
Value |  |  | 
0 | Master | MSB first | 32-bit
1 | Slave | LSB first | 
0x08 ~ 0x1F |  |  | 8-bit ~ 31-bit

## Slide 7: SPI基本功能设定 (II)
Function | Clock Polarity CLKP (SPI_CTL[11]) | Transmitting Edge TX_NEG (SPI_CTL[2]) | Receiving Edge RX_NEG (SPI_CTL[1])
Value |  |  | 
0 | SPICLK Idle Low | Positive-edge | Positive-edge
1 | SPICLK Idle High | Negative-edge | Negative-edge
支持通用的SPI Mode 0~3.

## Slide 8: SPI基本功能设定 (III)
Function | No Slave Select NOSLVSEL (SPI_SSR[5]) | Auto Slave Select AUTOSS (SPI_SSR[3]) | Slave Select Level Trigger SS_LTRIG (SPI_SSR[4]) | Slave Select Active Level SS_LVL (SPI_SSR[2])
Value |  |  |  | 
0 | 4-wire | Manual | Edge-trigger | Active-low
1 | 3-wire | Automatic | Level-trigger | Active-high

## Slide 9: 串行时钟
主:
  DIVIDER1 (SPI_CLKDIV[7:0]):
    SPI 串行时钟频率
  DIVIDER2 (SPI_CLKDIV[23:16]):
    SPI 串行时钟频率.
从:
  SPI时钟由片外主机提供. SPI 的时钟必须比主机的输入时钟快.
Is the SPI engine clock source (HCLK or PLL output)

## Slide 10: 可变时钟功能
VARCLK_EN (SPI_CTL[23]):
  VARCLK_EN = 1, 使能可变时钟功能.
  VARCLK_EN = 0, Disable.
只用于16-bit 数据长度.

## Slide 11: Word-/Byte暂停功能
SP_CYCLE (SPI_CTL[15:12]):
  暂停间隔由SP_CYCLE设定. (0.5~15.5 串行时钟周期)
Word-暂停功能只可用于FIFO 模式.
Byte-暂停功能只可用于 32-bit 数据长度.
Suspend interval

## Slide 12: 字节重排序功能
REORDER (SPI_CTL[20:19]):
  TX/RX FIFO 将被重新排序.

## Slide 13: 2-Bit (Two-Channel) 功能
TWOB (SPI_CTL[22]):

## Slide 14: 主模式下2-Bit 模式时序图
Channel 0
Channel 1

## Slide 15: 双IO 模式
DUAL_IO_EN (SPI_CTL[29]):
  =1, 使能双I/O模式.
  =0, 关闭.
DUAL_IO_DIR (SPI_CTL[28]):
  =1, 写数据.
  =0, 读数据.

## Slide 16: FIFO 模式
FIFO (SPI_CTL[21]):
  =1, FIFO 模式使能.
  =0, 关闭.

## Slide 17: 唤醒功能
从SPICLK收到来自外设的反转信号
  将芯片从power down 模式唤醒.

## Slide 18: 中断
INTEN (SPI_CTL[17]):
  1: 使能SPI 中断.
  0: 禁止SPI 中断.
中断标志:
INTSTS (SPI_STATUS[7]) | SLV_START_INTSTS (SPI_STATUS[6]) | TIME_OUT_STS (SPI_STATUS[12]) | TXINT_STS (SPI_STATUS[10]) | RXINT_STS (SPI_STATUS[8])
传输完成 | 3-Wrie 从机模式Start Event | 接收FIFO 超时 | 发送FIFO Event TX 缓冲中剩下的数据个数 <= TXTHRESHOLD. | 接收FIFO Event RX 缓冲中的数据个数 > RXTHRESHOLD

## Slide 19: 代码(I)
#define TEST_NUMBER 1 /* Page numbers */
#define TEST_LENGTH 256 /* Length */
uint8_t SrcArray[TEST_LENGTH];
uint8_t DestArray[TEST_LENGTH];
uint32_t volatile PDMA1_INT_Flag;
uint32_t volatile PDMA2_INT_Flag;
/* Main */
int main(void)
{
STR_PDMA_T sPDMA;
uint32_t u32ByteCount, u32FlashAddress, u32PageNumber;
uint32_t nError = 0;
SPI_DATA_T conf;
MFP_SPI0_TO_PORTE();
SPI_Init(SPI0);
/* Configure SPI0 as a master, 32-bit transaction*/
conf.u32Mode = SPI_MODE_MASTER;
conf.u32Type = SPI_TYPE0;
conf.i32BitLength = 32;
SPI_Open(SPI0, &conf);
/* Diable AutoSS */
SPI_DisableAutoSS(SPI0);

## Slide 20: 代码(II)
/* Set the active level of slave select. */
SPI_SetSlaveSelectActiveLow(SPI0);
/* SPI clock rate 1MHz */
SPI_SetClockFreq(SPI0, 1000000, 0);
/* PDMA Init */
PDMA_Init();
/* Configure PDMA Channel 1 to receive SPI0 Rx0 */
/* CH1 Setting */
PDMA_EnableChannelClock(PDMAGCR_CSR_CLK1); /* Enable Channel 1 Clock */
sPDMA.SrcAddr = (uint32_t)&(SPI0->RX0);
sPDMA.DestAddr = (uint32_t)&DestArray[0];
sPDMA.SrcCtrl = PDMA_CSR_SAD_FIX;
sPDMA.DestCtrl = PDMA_CSR_DAD_INC;
sPDMA.TransWidth = PDMA_CSR_APB_TWS_8BIT;
sPDMA.Mode = PDMA_CSR_IP2MEM;
sPDMA.ByteCnt = TEST_LENGTH;
sPDMA.IsTimeOutEnable = 0;
PDMA_Open(PDMA1, &sPDMA);
PDMA_SPI0_RX_TO_CH1();
/* Enable INT */
PDMA_EnableInt(PDMA1, PDMA_IER_TD);

## Slide 21: 代码(III)
/* Configure PDMA Channel 2 to receive SPI0 Tx0 */
/* Tx PDMA Setting */
PDMA_EnableChannelClock(PDMAGCR_CSR_CLK2); /* Enable Channel 2 Clock */
sPDMA.SrcAddr = (uint32_t)&SrcArray[0];
sPDMA.DestAddr = (uint32_t)&(SPI0->TX0);
sPDMA.SrcCtrl = PDMA_CSR_SAD_INC;
sPDMA.DestCtrl = PDMA_CSR_DAD_FIX;
sPDMA.TransWidth = PDMA_CSR_APB_TWS_8BIT;
sPDMA.Mode = PDMA_CSR_MEM2IP;
sPDMA.ByteCnt = TEST_LENGTH;
sPDMA.IsTimeOutEnable = 0;
PDMA_Open(PDMA2, &sPDMA);
PDMA_SPI0_TX_TO_CH2();
/* Enable INT */
PDMA_EnableInt(PDMA2, PDMA_IER_TD);
/* Read MID & DID */
if(SpiFlash_ReadMidDid() == 0)
printf(“MID and DID Error!!\n");
/* Erase SPI Flash */
SpiFlash_ChipErase();
/* Wait Ready */
SpiFlash_WaitReady();

## Slide 22: 代码(IV)
/* Program SPI Flash */
u32FlashAddress = 0;
for(u32PageNumber=0;u32PageNumber<TEST_NUMBER; u32PageNumber++){
/* Trigger PDMA Specified Channel */
PDMA_CHEnableTransfer(PDMA2);
/* Page Program */
SpiFlash_PageProgram(u32FlashAddress, 256);
SpiFlash_WaitReady();
u32FlashAddress += 0x100;
}
/* Read SPI Flash */
u32FlashAddress = 0;
for(u32PageNumber=0; u32PageNumber<TEST_NUMBER; u32PageNumber++){
/* Trigger PDMA Specified Channel */
PDMA_CHEnableTransfer(PDMA1);
/* Page Read */
SpiFlash_ReadData(u32FlashAddress, 256);
u32FlashAddress += 0x100;
for(u32ByteCount=0; u32ByteCount<256; u32ByteCount++){
if(DestArray[u32ByteCount] != SrcArray[u32ByteCount]){
printf("Data error! [%d] R:0x%x - W:0x%x\n", u32PageNumber, DestArray[u32ByteCount], SrcArray[u32ByteCount]);
nError ++;
}
}
}
if(nError == 0) printf("Compare Data OK!!\n");
}

## Slide 23: Thank you.