## Slide 1: NuMicro Nano Flash 控制器(FMC)
NuMicro@nuvoton.com
Notes: In the next topic, I will present the Flash Memory Controller

## Slide 2: 内容
Flash 控制器特性
Flash 映射
Data Flash
FMC 寄存器
ISP 命令
用户配置
启动选择
In System Programming (ISP)
In Application Programming (IAP)
范例

## Slide 3: Flash 内存特性
APROM 123/64/32 KB
4KB in system programming 空间(LDROM) for ISP loader
Data flash 起始地址和大小可以编程
页擦除单位512 bytes
支持PDMA 读 Data Flash

## Slide 4: Flash 内存映射

## Slide 5: Data Flash

## Slide 6: FMC 寄存器
Register | Offset | R/W | Description | Reset Value
Base Address (FMC_BA) : 0x5000_C000 |  |  |  | 
ISPCON | 0x00 | R/W | ISP 控制寄存器 | 0x0000_0000
ISPADR | 0x04 | R/W | ISP 地址寄存器 | 0x0000_0000
ISPDAT | 0x08 | R/W | ISP 数据寄存器 | 0x0000_0000
ISPCMD | 0x0C | R/W | ISP 命令寄存器 | 0x0000_0000
ISPTRG | 0x10 | R/W | ISP 触发寄存器 | 0x0000_0000
DFBADR | 0x14 | R | Data Flash 起始地址 | User Config1
ISPSTA | 0x40 | R/W | ISP 状态寄存器 | 0x0000_0000

## Slide 7: ISPCON
Bits | Descriptions | 
[31:7] | - | Reserved
[6] | ISPFF | ISP Fail Flag
[5] | LDUEN | LDROM Update Enable
[4] | CFGUEN | Enable Config-bits Update by ISP
[3] | APUEN | APROM Update Enable
[2] | - | Reserved
[1] | BS | Boot Select (1:LDROM; 0:APROM)
[0] | ISPEN | ISP Enable

## Slide 8: ISPADR
Bits | Descriptions | 
[31:0] | ISP Address | ISP erase/program/read address
ISPDAT
Bits | Descriptions | 
[31:0] | ISP Data | ISP program/read data word

## Slide 9: ISPCMD
Bits | Descriptions | 
[31:6] | Reserved | 
[5] | FOEN | 
[4] | FCEN | 
[3:0] | FCTRL | 
Operation Mode | FOEN | FCEN | FCTRL[3:0]
Read | 0 | 0 | 0x0
Vector Page Remap | 1 | 0 | 0xE
Program | 1 | 0 | 0x1
Page Erase | 1 | 0 | 0x2
Read CID | 0 | 0 | 0xB
Read DID | 0 | 0 | 0xC
Read UID/UCID | 0 | 0 | 0x4

## Slide 10: ISPTRG
Bits | Descriptions | 
[31:1] | Reserved | 
[0] | ISPGO | ISP start trigger
DFBADR
Bits | Descriptions | 
[31:0] | DFBA | Data Flash Base Address

## Slide 11: ISPSTA
Bits | Descriptions | 
[31:21] | Reserved | 
[20:9] | VECMAP | Vector Page Mapping Address
[8:7] | Reserved | 
[6] | ISPFF | ISP Fail flag
[5:3] | Reserved | 
[2:1] | CBS | Boot Selection Status
[0] | ISPBUSY | ISP BUSY

## Slide 12: ISP 命令
Enable DFEN/LDUEN
5 Commamds :
1. Read
2. Program
3. Page Erase
4. Read CID
5. Read DID
If ISPFF(Fail Flag) = 1,
it means the one of the follow conditions.
1. APROM writes to itself.
2. LDROM writes to itself.
3. CONFIG is erased/programmed when
the MCU is running in APROM if CFGUEN is set to 0.
4. Destination address is illegal,
such as over an available range.

## Slide 13: 擦除
int32_t DrvFMC_Erase(uint32_t u32addr)
{
FMC->ISPCMD = 0x22;
FMC->ISPADR = u32addr; /* 512 bytes aligned page address */
FMC->ISPTRG_BITS.ISPGO = 1;
while (FMC->ISPTRG_BITS.ISPGO) ;
if (FMC->ISPCON_BITS.ISPFF == 1) {
FMC->ISPCON_BITS.ISPFF = 1;
return E_DRVFMC_ERR_ISP_FAIL;
}
return 0;
}

## Slide 14: 编程
int32_t DrvFMC_Write(uint32_t u32addr, uint32_t u32data)
{
FMC->ISPCMD = 0x21;
FMC->ISPADR = u32addr; /* word aligned */
FMC->ISPDAT = u32data;
FMC->ISPTRG_BITS.ISPGO = 1;
while (FMC->ISPTRG_BITS.ISPGO) ;
if (FMC->ISPCON_BITS.ISPFF == 1) {
FMC->ISPCON_BITS.ISPFF = 1;
return E_DRVFMC_ERR_ISP_FAIL;
}
return 0;
}

## Slide 15: 读
int32_t DrvFMC_Read(uint32_t u32addr, uint32_t *u32data)
{
FMC->ISPCMD = 0x00;
FMC->ISPADR = u32addr; /* word aligned */
FMC->ISPTRG_BITS.ISPGO = 1;
while (FMC->ISPTRG_BITS.ISPGO) ;
if (FMC->ISPCON_BITS.ISPFF == 1) {
FMC->ISPCON_BITS.ISPFF = 1;
return E_DRVFMC_ERR_ISP_FAIL;
}
*u32data = FMC->ISPDAT;
return 0;
}

## Slide 16: 用户配置区 – Config0
Bits | Descriptions | 
[31:27] | Reserved | Reserved
[26] | CFOSC | CPU Clock Source Select After Reset 0: External 12MHz crystal clock, 1: Internal RC 12MHz oscillator clock
[25:21] | Reserved | Reserved
[20:19] | CBORST | Brown Out Reset Enable 00: BOD17 reset enable 01: BOD20 reset enable 10: BOD25 reset enable 11: Reserved
[18:8] | Reserved | Reserved

## Slide 17
Bits | Descriptions | 
[7:6] | CBS | Config Boot Selection 11: APROM(LDROM invisible) 01: LDROM(APROM invisible) 10: CPU boot from APROM. 00: CPU boot from LDROM. Memory 0x0000_0000~0x0000_01FF be re-mapped to page 0 of LDROM.
[5:2] | Reserved | Reserved
[1] | LOCK | Security Lock 0 = Flash data is locked 1 = Flash data is not locked. When flash data is locked, only device ID, Config0 and Config1 can be read by writer and ICP thru serial debug interface. Others data is locked as 0xFFFFFFFF. ISP can read data anywhere regardless of LOCK bit value.
[0] | DFEN | Data Flash Enable 0 = Enable data flash 1 = Disable data flash

## Slide 18: 用户配置区 – Config1
Bits | Descriptions | 
[31:20] | Reserved | Reserved
[19:0] | DFBA | Data Flash Base Address The data flash base address is defined by user.

## Slide 19: 启动选择
启动选择由Config0 CBS[1:0]决定.
在Power-On 复位, BOD复位, WDT复位, RTC复位, ... FMC 将加载Config0 CBS[1] to ISPCON->BS bit.
CPU 复位和系统复位, FMC 不会加载Config0 CBS to ISPCON->BS bit.
用户可以通过设定ISPCON->BS bit 并执行 CPU 复位来动态切换启动模式(APROM or LDROM).

## Slide 20: 启动模式& 内存映射

## Slide 21: In System Programming (ISP)
ISP 的目的是提供一种方法便于更新APROM中的应用程序.
ISP 程序放在LDROM中. 客户程序放在APROM中.
ISP Master (PC or NuMicro board)通过UART/USB/I2C/SPI控制ISP 程序.

## Slide 22: ISP 流程

## Slide 23: In Application Programming (IAP)
支持所有的ISP 功能.
可以更新应用程序，不用复位系统
设定CBS=10b or 00b
程序可以在 APROM 和LDROM之间跳转.
没有 data flash. LDROM 和APROM 的任何地方都可以用作data area.

## Slide 24: IAP 流程 (CBS=00b)

## Slide 25: IAP 流程 (CBS=10b)

## Slide 26: 范例
SMPL_FMC_DEMO
  编译isp and ld_boot firstly
  编译ap_demo.
  写ap_demo.bin to APROM
  运行.

## Slide 27: ap_image.s
Include bin file to image

## Slide 28: ap_demo.c
/*---------------------------------------------------------------------------------------------------------*/
/* Main Function */
/*---------------------------------------------------------------------------------------------------------*/
int32_t main (void)
{
...
UNLOCKREG();
FMC_Init();
FMC_EnableLDUpdate();
if (load_image_to_flash((uint32_t)&loaderImage1Base, (uint32_t)&loaderImage1Limit, LDROM_BASE, LDROM_SIZE) != 0)
{
printf("Load image to LDROM failed!\n");
return -1;
}
FMC_DisableLDUpdate();
FMC->ISPCON |= FMC_ISPCON_APUEN; // FMC Enable APUpdate
if (load_image_to_flash((uint32_t)&loaderImage2Base, (uint32_t)&loaderImage2Limit, ISP_BASE, ISP_MAX_SIZE) != 0)
{
printf("Load image to APROM failed!\n");
return -1;
}

## Slide 29: ap_demo.c(CONT’)
29
FMC_EnableConfigUpdate();
config0 = (config0 & ~0xc0); /* set CBS to 00b */
FMC_Erase(CONFIG0);
FMC_Write(CONFIG0, config0 | 0x2);
FMC_Write(CONFIG1, config1);
FMC_DisableConfigUpdate();
// do chip reset
GCR->IPRST_CTL1 |= GCR_IPRSTCTL1_CHIP;
}

## Slide 30: ld_boot 选择

## Slide 31: Startup_nano1xx_vecmap_1M.s
Enable Vector Page Remap

## Slide 32: ld_boot代码
32
#define USER_AP_ENTRY (0)
#define ISP_CODE_ENTRY (50*1024)
typedef void (FUNC_PTR)(void);
int32_t main (void)
{
FUNC_PTR *func;
....
func = (FUNC_PTR *)(*(uint32_t *)(ISP_CODE_ENTRY+4));
FMC_SetVectorPage(0x0);
func();
....
func = (FUNC_PTR *)(*(uint32_t *)(USER_AP_ENTRY+4));
FMC_SetVectorPage(0x0);
func();
}

## Slide 33: ISP 选项

## Slide 34: isp_image.s
Include bin file to image

## Slide 35: ISP.c
35
#define USER_AP_MAX_SIZE (50*1024)
#define USER_AP_ENTRY (0)
#define ISP_CODE_ENTRY (50*1024)
#define LD_BOOT_CODE_ENTRY 0x100000
#define PAGE_SIZE 512
typedef void (FUNC_PTR)(void);
int32_t main (void)
{
FUNC_PTR *func;
…
func = (FUNC_PTR *)(*(uint32_t *)(LD_BOOT_CODE_ENTRY+4));
FMC_SetVectorPage(0x100000);
func();
…
func = (FUNC_PTR *)(*(uint32_t *)(USER_AP_ENTRY+4));
FMC_SetVectorPage(0x0);
func();
…

## Slide 36: ISP.c (CONT’)
36
FMC->ISPCON |= FMC_ISPCON_APUEN; // FMC_EnableAPUpdate();
if (load_image_to_flash((uint32_t)&ApImage1Base, (uint32_t)&ApImage1Limit,
USER_AP_ENTRY, USER_AP_MAX_SIZE) != 0)
{
printf("Load image to APROM failed!\n");
return -1;
}
FMC->ISPCON &= ~FMC_ISPCON_APUEN; // FMC_DisableAPUpdate();
func = (FUNC_PTR *)(*(uint32_t *)(USER_AP_ENTRY+4));
FMC_SetVectorPage(0x0);
func();
…
}

## Slide 37
Thank you