## Slide 1: NuMicro Nano I2S
NuMicro@nuvoton.com

## Slide 2: 内容
I2S 介绍
I2S 特性
I2S 时钟源
I2S 方块图
I2S 时序
FIFO 结构
范例

## Slide 3: I2S 介绍
I2S (Inter-IC Sound or Integrated Interchip Sound)
Interface Signals
  BCLK: (Bit Clock Line)
  LRCLK: (Word Clock Line, Word Select Line)
    Left/Right channel selection
  SDI: (Serial Data Input)
    To receive the ADC data
  SDO: (Serial Data Output)
    To send the audio PCM data to DAC
Application:
  To connect with external audio codec

## Slide 4: I2S 特性
I2S can operate as either master or slave mode
Capable of handling 8, 16, and 32 bit word sizes.
Supports mono and stereo audio data.
Supports I2S and MSB justified data format.
Provides two 8 words FIFO data buffers, one for transmit and one for receive.
Generates interrupt requests when buffer levels cross a programmable boundary.
Two DMA requests, one for transmit and one for receive

## Slide 5: 方块图
I2S_BCLK = I2S_CLK /(2x(BCLK_DIV[7:0] + 1))
I2S_MCLK = I2S_CLK/(2x(MCLK_DIV[2:0]))
I2S_MCLK = I2S_CLK/(2x(MCLK_DIV[2:0]))

## Slide 6: I2S 总线时序: Format 0
Data Delay 1 BCLK

## Slide 7: I2S 总线时序: Format 1 (MSB Justified)

## Slide 8: 寄存器
Register | Offset | R/W | Description | Reset Value
I2S_BA = 0x401A_0000 |  |  |  | 
I2S_CTRL | I2S_BA+0x00 | R/W | I2S Control Register | 0x0000_0000
I2S_CLKDIV | I2S_BA+0x04 | R/W | I2S Clock Divider Register | 0x0000_0000
I2S_INTEN | I2S_BA+0x08 | R/W | I2S Interrupt Enable Register | 0x0000_0000
I2S_STATUS | I2S_BA+0x0C | R/W | I2S Status Register | 0x0014_1000
I2S_TXFIFO | I2S_BA+0x10 | R/W | I2S Transmit FIFO Register | 0x0000_0000
I2S_RXFIFO | I2S_BA+0x14 | R/W | I2S Receive FIFO Register | 0x0000_0000

## Slide 9: 发送 FIFO 结构
TX FIFO
(8x32 bits)
CPU (Write)
Threshold
What FIFO status are available in the status register?
  FIFO Empty
  FIFO Full
  Arrive threshold level
  Overflow
  Underflow
TX Transmitter (Read)
I2S Status Register (I2S_STATUS)
Register | Offset | R/W | Description | Reset Value
I2S_STATUS | I2S_BA + 0x0C | R/W | I2S Status Register | 0x0014_1000

## Slide 10: 接收FIFO 结构
RX FIFO
(8x32 bits)
I2S Receiver (Write)
Threshold
CPU (Read)
I2S Status Register (I2S_STATUS)
Register | Offset | R/W | Description | Reset Value
I2S_STATUS | I2S_BA + 0x0C | R/W | I2S Status Register | 0x0014_1000
What FIFO status are available in the status register?
  FIFO Empty
  FIFO Full
  Arrive threshold level
  Overflow
  Underflow

## Slide 11: 不同数据模式下数据结构
Mono Format
Stereo Format

## Slide 12: I2S 中断
Threshold
Overflow
Underflow
Threshold
Overflow
Underflow
Zero Crossing

## Slide 13: 范例: 连接WAU8822 Codec

## Slide 14: 代码(1/2)
/*Set multi function pin for I2S GPC0, GPC1, GPC2, GPC3, GPA15 */
MFP_I2S_TO_PORTC();
/* === Use I2C0 to communicate with WAU8822 === */
/* Set multi function pin for I2C0 */
GCR->PA_H_MFP = GCR->PA_H_MFP & ~(PA8_MFP_MASK|PA9_MFP_MASK) |
PA8_MFP_I2C0_SDA | PA9_MFP_I2C0_SCL;
I2C_Init(I2C0);
/* Open I2C0 and set clock = 100Kbps */
I2C_Open(I2C0, 100000);
/* Enable I2C0 interrupt and set corresponding NVIC bit */
I2C_EnableInt(I2C0);
I2S_Init();
st.u32SampleRate = 16000;
st.u32WordWidth = I2S_DATABIT_16;
st.u32AudioFormat = I2S_MONO;
st.u32DataFormat = I2S_FORMAT_I2S;
st.u32Mode = I2S_MODE_SLAVE;
st.u32TxFIFOThreshold = I2S_FIFO_TX_LEVEL_WORD_4;
st.u32RxFIFOThreshold = I2S_FIFO_RX_LEVEL_WORD_4;
I2S_Open(&st);
To set these parameter to I2S control register

## Slide 15: 代码(2/2)
// select source from HXT(12MHz)
SYS_SelectIPClockSource_2(CLK_CLKSEL2_I2S_MASK, CLK_CLKSEL2_I2S_HXT);
// div = 0
SYS_SetClockDivider_0(CLK_CLKDIV0_I2S_MASK, I2S_CLK_DIVIDER(0));
/* Initialize WAU8822 codec */
WAU8822_Setup();
/* Set MCLK and enable MCLK */
I2S_SetMCLKFreq(12000000);
I2S_EnableMCLK();
/* Enable Rx threshold level interrupt */
I2S_EnableInt_RxThreshold();
/* Enable I2S Rx function to receive data */
I2S_EnableRx();
while(1)
{
if (u32startFlag)
{
/* Enable I2S Tx function to send data when data in the buffer is more than half of buffer size */
if (u32BuffPos >= BUFF_LEN/2)
{
I2S_EnableInt_TxThreshold();
I2S_EnableTx();
u32startFlag = 0;
}
}
}

## Slide 16
Thank you